## Slide 1
Energy-Driven Physics-Informed Neural Network for Multilayer MEMS Diaphragm Pressure Sensors
Föppl–von Kármán Variational Formulation | Classical Laminated Plate Theory | Hard Boundary Conditions | Contact Enforcement
Parylene-C / Gold / Parylene-C · Circular Clamped Diaphragm · Capacitive Sensor
1 / 11

## Slide 2
1. Motivation & Problem Statement
2 / 11
▸ Device
  – Clamped circular diaphragm: parylene-C / Au / parylene-C
  – Radius a = 150–500 µm, air gap ag = 5–15 µm
  – Uniform pressure P = 10 Pa – 20 kPa
▸ Goal
  – Predict full deflection profile w(r) for any geometry & pressure
  – Without re-running COMSOL for each new design
▸ Challenge: large deflections
  – w/h can reach 5–10× → linear plate theory fails
  – Membrane stiffening must be captured
  – Contact with electrode at w = −ag must be enforced
▸ Why not just FEA?
  – COMSOL: minutes–hours per geometry point
  – Design optimisation needs 10³–10⁴ evaluations
  – Surrogate model gives <1 ms inference
▸ Why not Kirchhoff (Atik analytical)?
  – w(r) = −Pa⁴/(64D*) · (1−ξ²)²
  – Valid only for w << thickness
  – Ignores membrane stiffening → overestimates deflection
  – No contact enforcement
▸ Approach
  – PINN trained by minimising the physical energy functional
  – No labelled data required during main training

## Slide 3
2. Governing Physics: Föppl–von Kármán (FvK)
3 / 11
▸ Kirchhoff (linear) plate theory — valid only for w << h
  – Bending stiffness D* resists deflection
  – Equilibrium: D∇⁴w + P = 0
▸ FvK extension — large deflections
  – Plate also stretches in-plane as it bends
  – In-plane tension (membrane stiffening) increases effective stiffness
  – Two coupled unknowns: w(r) transverse, u(r) radial in-plane
▸ Nonlinear membrane strains (the key physics)
  – εᵣ = u'(r) + ½(w'(r))² ← ½(w')² is the geometric nonlinearity
  – εθ = u(r) / r
  – Dropping u or the ½(w')² term loses all membrane stiffening
▸ No closed-form solution for general multilayer geometry → need a surrogate
Bending energy density:
½ D* (w'' + w'/r)²
Membrane energy density:
½ [A₁₁εᵣ² + 2A₁₂εᵣεθ + A₁₁εθ²]
Pressure work density:
P · w (w < 0 → decreases Π)
D*, A₁₁, A₁₂ from Classical Laminated Plate Theory (computed analytically)

## Slide 4
3. Material Model: Classical Laminated Plate Theory (CLT)
4 / 11
▸ 3-layer stack: parylene-C / gold / parylene-C
  – Parylene-C: E = 3.2 GPa, ν = 0.33
  – Gold: E = 70 GPa, ν = 0.44 (22× stiffer)
▸ Neutral axis z_NA
  – z_NA = Σ Ēₖ tₖ z_{c,k} / Σ Ēₖ tₖ
  – Gold is stiff and not at geometric midplane
  – Pulls z_NA upward → asymmetric bending stiffness
▸ Effective bending stiffness D*
  – D* = (1/3) Σ Ēₖ (bₖ³ − bₖ₋₁³)
  – bₖ = signed distance from z_NA to layer top
  – Cubic: thin gold far from NA contributes like I-beam flange
▸ Membrane stiffness A₁₁, A₁₂
  – A₁₁ = Σ Ēₖ tₖ (axial)
  – A₁₂ = Σ νₖ Ēₖ tₖ (Poisson coupling)
▸ Why compute CLT analytically, not learn it?
  – D*, A₁₁, A₁₂ are exact — no approximation needed
  – Embedding exact physics reduces what the network must learn
  – Generalises outside training range without extrapolation error
▸ Nominal values (t1=1, t2=0.2, t3=4 µm)
  – z_NA = 1.89 µm (geometric midplane = 2.6 µm)
  – D* = 6.19 × 10⁻⁸ N·m
  – A₁₁ = 3.53 × 10⁴ N/m
  – ν_eff = A₁₂/A₁₁ = 0.384
▸ Computed fresh for every training batch
  – Geometry (t1, t2, t3) is sampled stochastically each step
  – D*, A₁₁, A₁₂ evaluated analytically at batch geometry

## Slide 5
4. Training Signal: Variational Energy Functional
5 / 11
▸ Total potential energy
  – Π[w, u] = ∫₀ᵃ 2πr [ ½D*(w''+w'/r)² + ½(A₁₁εᵣ² + 2A₁₂εᵣεθ + A₁₁εθ²) + Pw ] dr
▸ Why energy, not PDE residual?
  – Energy is a single scalar — simpler gradient signal than pointwise PDE enforcement
  – At the minimum, δΠ/δw = 0 recovers D∇⁴w + P = 0 (FvK Euler–Lagrange)
  – Natural boundary conditions satisfied automatically at the minimum
  – No labelled data needed — physics alone constrains the solution
▸ Why +Pw (not −Pw)?
  – w < 0 for downward deflection → Pw < 0 → decreases Π as plate deflects
  – Energy minimisation drives the plate downward — physically correct
  – Wrong sign locks the network at w = 0 (deflection is energetically unfavourable)
▸ Numerical integration: 32-node Gauss–Legendre quadrature on ξ ∈ (0, 1)
  – Differentiable weighted sum → backpropagation flows through the integral
  – ξ = 0 excluded — avoids 1/r singularity in εθ = u/r
  – Exponentially accurate for smooth (tanh) networks — 32 nodes is sufficient
▸ Per-sample energy normalisation (critical for multi-scale training)
  – Energy at P = 20 kPa ~ 10⁻⁸ J vs P = 50 Pa ~ 10⁻¹² J → 4 orders of magnitude
  – Π_norm = Π_i / |Π_i| → every sample contributes ±1 to the gradient
  – Without this: P = 100 Pa error = 232% | with this: 2.2%

## Slide 6
5. Network Architecture
6 / 11
▸ Input: 7 normalised features [ξ, P̂, t̂₁, t̂₂, t̂₃, â, âg]
  – ξ = r/a (radial coordinate, already in [0,1] — network learns shapes, not sizes)
  – P̂ = log(1 + P/1000) / log(21) — log-scale: 10 Pa–20 kPa span 3 decades
  – t̂₁, t̂₂, t̂₃, â, âg — min-max to [0,1] within training geometry range
▸ Trunk: 6 fully-connected layers, 128 neurons, Tanh activation throughout
  – Why Tanh? Bending energy needs w'' (second autograd derivative through the network)
  – ReLU → w'' = 0 almost everywhere → no bending energy gradient
  – GELU → w'' noisy and oscillatory → unstable energy computation
  – Tanh → smooth, analytic, well-behaved second derivatives → stable training
▸ Two independent output heads (Linear 128→1 each)
  – Head w → transverse deflection w(r) [the observable]
  – Head u → radial in-plane displacement u(r) [needed for εᵣ = u' + ½(w')²]
  – Without u: εᵣ = ½(w')² only → misses actual in-plane displacement → wrong stiffness
▸ ~100 k parameters total | float32 | trained on GPU
Input [7]
↓ Linear(7→128) + Tanh
↓ Linear(128→128) + Tanh ×5
↓
┌──────────┬──────────┐
head_w head_u
Lin(128→1) Lin(128→1)
↓ ↓
hard BC hard BC
↓ ↓
w(r) [m] u(r) [m]
Xavier uniform init Zero-init output heads

## Slide 7
6. Hard Boundary Conditions & Contact Constraint
7 / 11
▸ Clamped rim: algebraic enforcement
  – w_profile = (1 − ξ²)² · w_raw · W_ref
  – (1−ξ²)² is the exact Kirchhoff clamped-plate polynomial
  – Guarantees: w(ξ=1) = 0, w'(ξ=1) = 0, symmetry at ξ = 0
  – Whatever the network outputs, BCs are mathematically exact
▸ In-plane BC
  – u = ξ(1−ξ) · u_raw · U_ref
  – Guarantees: u(0) = 0 (symmetry), u(1) = 0 (clamped rim)
▸ Why hard BCs instead of soft BC penalty?
  – Soft penalty: BCs can still be violated; extra hyperparameter
  – Hard BC: zero gradient budget wasted on BC enforcement
  – All network capacity goes toward learning interior physics
▸ Physical output scaling: W_ref = ag_phys
  – Maximum deflection is −ag → w_raw lives in O(1)
  – Consistent across all geometries regardless of ag
▸ Contact constraint: w ≥ −ag
  – Smooth-max: w = ½(w_p + (−ag) + √((w_p−(−ag))² + ε²))
  – ε = 50 nm → transition width at contact line
▸ Why not torch.clamp(w, min=−ag)?
  – clamp: gradient = 0 in contact zone
  – Network receives no learning signal where plate touches electrode
  – Smooth-max: gradient nonzero everywhere → learns contact physics
▸ Why not κ-obstacle penalty?
  – Contact penalty ~10⁻¹² J vs pressure work ~10⁻⁸ J at 15 kPa
  – Ratio 1:10,000 → constraint dominated by pressure term
  – Even at κ = 10¹⁰: still 1.9 µm penetration
▸ Smooth-max result
  – Hard mathematical guarantee: w ≥ −ag to within 50 nm
  – 0 / 200 penetration violations across random geometry sweep

## Slide 8
7. Training Strategy
8 / 11
▸ Geometry sampling (each step)
  – 64 geometries × 8 pressures = 512 samples per step
  – t1, t3 ~ Uniform[1–5 µm], t2 ~ [0.2–0.5 µm]
  – a ~ Uniform[150–500 µm], ag ~ [5–15 µm]
  – P ~ Log-Uniform[10 Pa – 20 kPa]
▸ COMSOL warmup (steps 0–5000, λ annealing 1→0)
  – Anchors network in correct deflection regime
  – Prevents spurious minima (flat plate, upward deflection)
  – L_total = L_energy + λ · L_COMSOL_MSE
  – After step 5000: λ = 0, pure physics only
▸ Optimiser: Adam
  – LR: 1×10⁻³ (warmup) → cosine decay to 1×10⁻⁴
  – Gradient clipping: max_norm = 1.0
  – 50 000 steps total | ~55 min on GPU
▸ Why stochastic geometry sampling?
  – Network must generalise over 5D geometry space
  – Random sampling covers the space without grid explosion
  – 5D uniform grid at 10 pts/dim = 10⁵ points → impractical
▸ Why log-uniform pressure sampling?
  – Three-decade range: 10 Pa – 20 kPa
  – Linear sampling starves low-P regime
  – Log-uniform: equal samples per decade
▸ Why gradient clipping?
  – Energy gradient can spike at initialisation (random w far from equilibrium)
  – Clipping prevents early instability without affecting steady-state
▸ Loss history
  – L_energy converges from ~+1 (random init) to ~−0.7
  – Negative energy: pressure work dominates → physically correct

## Slide 9
8. Results: Deflection Profiles — 5 Geometries
9 / 11
▸ Three-way comparison: PINN (solid) | COMSOL FEA (dashed) | Atik/Kirchhoff (dotted)
▸ 5 geometries spanning the design space
  – Small thin a=227 µm, t1/t3=1.6/1.1 µm, ag=6.0 µm
  – Medium balanced a=290 µm, t1/t3=1.7/2.1 µm, ag=7.9 µm
  – Large thick a=460 µm, t1/t3=4.3/3.9 µm, ag=11.1 µm
  – Small large gap a=179 µm, t1/t3=1.7/2.1 µm, ag=13.1 µm
  – Large thin a=462 µm, t1/t3=1.6/1.7 µm, ag=5.4 µm
▸ Key observations
  – Low pressure (500 Pa): all three methods agree → linear regime
  – High pressure (10–20 kPa): Atik overestimates deflection (dotted below solid/dashed)
  – Membrane stiffening captured by PINN/COMSOL → less deflection than Kirchhoff predicts
  – Touch-mode: PINN & COMSOL both plateau at w = −ag; Atik is clipped artificially
  – Atik predicts touch-down at lower pressure than reality (ignores membrane stiffening)
▸ PINN vs COMSOL agreement is the key validation
  – Solid and dashed nearly overlapping across all pressures and geometries

## Slide 10
9. Quantitative Validation — 2144 COMSOL Files
10 / 11
▸ Validation set
  – 2144 COMSOL deflection profiles
  – Geometries span the full 5D training box
  – 8 pressures per geometry (500 Pa → 20 kPa)
▸ RMSE: PINN vs COMSOL (µm)
  – Median RMSE: 0.15 µm
  – Mean RMSE: 0.22 µm
  – p90 RMSE: 0.51 µm
  – Max RMSE: 1.10 µm (worst: a ≈ 492 µm, boundary)
▸ Linear regime accuracy
  – P = 100 Pa Kirchhoff error (w_PINN vs w_exact): 2.2%
  – Confirms energy minimum recovers correct PDE solution
▸ Contact enforcement
  – 0 / 200 penetration violations in random geometry sweep
  – Hard smooth-max constraint holds across full pressure range
▸ Error breakdown by pressure
  – Low P (≤ 1 kPa): RMSE < 0.05 µm (linear regime, easy)
  – Mid P (1–5 kPa): RMSE 0.1–0.3 µm (membrane stiffening onset)
  – High P (≥ 10 kPa): RMSE 0.3–1.1 µm (touch mode, hardest)
▸ What drives the remaining error?
  – Large-plate geometries (a > 400 µm) show highest RMSE
  – Near training-box boundary → less training coverage
  – Touch-mode transition radius prediction (contact area boundary)
▸ Context
  – Air gap range: 5–15 µm → RMSE / ag = 1–7%
  – Comparable or better than other PINN plate surrogates
  – Inference: < 1 ms vs COMSOL: minutes per point

## Slide 11
10. Conclusions & Design Decisions
11 / 11
▸ What was built
  – PINN surrogate for multilayer MEMS diaphragm over 5D geometry space
  – Trained purely on physics energy (no FEA labels in main training)
  – Median RMSE 0.15 µm vs COMSOL, 0 contact violations
▸ Key design decisions (and why)
  – Tanh activations → clean autograd second derivatives for bending energy
  – Two heads (w, u) → correct FvK membrane strain εᵣ = u' + ½(w')²
  – Hard BCs (1−ξ²)² → exact enforcement, no wasted gradient budget
  – Smooth-max contact → hard guarantee + nonzero gradient in touch mode
  – Per-sample energy normalisation → equal learning across 4-decade pressure range
  – Log-scale pressure input → equal representation of all pressure decades
  – W_ref = ag → O(1) network outputs across all air-gap geometries
▸ What the figures show
  – PINN ≈ COMSOL at all pressures and geometries → surrogate is valid
  – Kirchhoff overestimates deflection at P > 1 kPa → FvK is necessary
  – Touch-mode correctly captured; contact radius matches COMSOL
▸ Limitations
  – Max RMSE 1.10 µm for large plates (a > 400 µm)
  – Touch-mode transition slightly imprecise at very high P
▸ Possible extensions
  – Wider network (256-dim) or 100k steps to close large-plate gap
  – Capacitance C(P) prediction directly from w(r) (Eroglu 2025)
  – Extend to elliptical or rectangular diaphragm geometries
  – Uncertainty quantification via ensemble or dropout